## Slide 1: Hardware of iMOSS
Zengyou Ye
https://www.github.com/addy9908/iMOSS
Updated on 05/13/2026

## Slide 2: iMOSS workflow
Load Cell
Amplifier
Arduino Uno
iMOSS-AS
iMOSS-MV
Bonsai-RX
(Monitor & save)
TST
Chamber
Synchronized
Acquisition
Offline
Analysis
TTL
White Noise

## Slide 3: Material list
Category | Item Description | Catalog # | Unit Price | QT
Box (canalplastic) | White Opaque Acrylic Sheet: 5.5 x 5 x 1/8” (stage) |  | $3.60 | 4
 | White Opaque Acrylic Sheet: 22 x 5 x 1/8” (divider) |  | $7.20 | 5
 | White Opaque Acrylic Sheet: 24 x 10 x 1/4” (base) |  | $24.00 | 1
 | White Opaque Acrylic Sheet: 24 x 22 x 1/4” (back) |  | $48.00 | 1
Stage holder (Amazon) | 16U Vertical Server Rack Rail |  | $27.98 | 1
Electronic (sparkfun) | Mini Load Cell - 100g | 14727 | $9.95 | 4
 | Load Cell Amplifier - HX711 | 13879 | $10.95 | 4
 | Arduino Uno R3 | DEV-11021 | $27.60 | 1
3D parts (self-printed) | Load cell holder: base |  |  | 4
 | Load cell holder: top |  |  | 4

## Slide 4: iMOSS-AS hardware module
Arduino
Uno
R3
Load Cell
Load
Cell AMP
RED
BLK
WHT
GRN
YLW
VDD
VCC
DAT
CLK
GND
5V
5V
Pin8
Pin9
GND
Load Cell
Load
Cell AMP
RED
BLK
WHT
GRN
YLW
VDD
VCC
DAT
CLK
GND
5V
5V
Pin6
Pin7
GND
Load Cell
Load
Cell AMP
RED
BLK
WHT
GRN
YLW
VDD
VCC
DAT
CLK
GND
5V
5V
Pin2
Pin3
GND
Load Cell
Load
Cell AMP
RED
BLK
WHT
GRN
YLW
VDD
VCC
DAT
CLK
GND
5V
5V
Pin4
Pin5
GND
CUT AMP for 80 Hz
Note: To archive 80Hz sampling rate, we need to cut the back of load cell amplifier

## Slide 5: Bonsai workflow